## Slide 1: CS 61C: Great Ideas in Computer Architecture Finite State Machines, Functional Units
Instructors:
John Wawrzynek & Vladimir Stojanovic
http://inst.eecs.Berkeley.edu/~cs61c/fa15

## Slide 2: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions

## Slide 3: Type of Circuits
Synchronous Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL) circuits
    Output is a function of the inputs only, not the history of its execution
    E.g., circuits to add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    aka “State Elements”
    E.g., memories and registers (Registers)

## Slide 4: Uses for State Elements
Place to store values for later re-use:
  Register files (like $1-$31 in MIPS)
  Memory (caches and main memory)
Help control flow of information between combinational logic blocks
  State elements hold up the movement of information at input to combinational logic blocks to allow for orderly passage

## Slide 5: Accumulator Example
Want: S=0;
for (i=0;i<n;i++)
S = S + Xi
Why do we need to control the flow of information?
Assume:
  Each X value is applied in succession, one per cycle
  After n cycles the sum is present on S
SUM
Xi
S

## Slide 6: First Try: Does this work?
No!
Reason #1: How to control the next iteration of the ‘for’ loop?
Reason #2: How do we say: ‘S=0’?
Feedback

## Slide 7: Register Internals
n instances of a “Flip-Flop”
Flip-flop name because the output flips and flops between 0 and 1
D is “data input”, Q is “data output”
Also called “D-type Flip-Flop”

## Slide 8: Flip-Flop Operation
Edge-triggered d-type flip-flop
  This one is “positive edge-triggered”
“On the rising edge of the clock, the input d is sampled and transferred to the output. At all other times, the input d is ignored.”
Example waveforms:

## Slide 9: Flip-Flop Timing
Edge-triggered d-type flip-flop
  This one is “positive edge-triggered”
“On the rising edge of the clock, the input d is sampled and transferred to the output. At all other times, the input d is ignored.”
Example waveforms (more detail):

## Slide 10: Camera Analogy Timing Terms
Want to take a portrait – timing right before and after taking picture
Set up time – don’t move since about to take picture (open camera shutter)
Hold time – need to hold still after shutter opens until camera shutter closes
Time click to data – time from open shutter until can see image on output (viewscreen)

## Slide 11: Hardware Timing Terms
Setup Time: when the input must be stable before the edge of the CLK
Hold Time: when the input must be stable after the edge of the CLK
“CLK-to-Q” Delay: how long it takes the output to change, measured from the edge of the CLK

## Slide 12: Accumulator Timing 1/2
Reset input to register is used to force it to all zeros (takes priority over D input).
Si-1 holds the result of the ith-1 iteration.
Analyze circuit timing starting at the output of the register.

## Slide 13: Accumulator Timing 2/2
reset signal shown.
Also, in practice X might not arrive to the adder at the same time as Si-1
Si temporarily is wrong, but register always captures correct value.
In good circuits, instability never happens around rising edge of clk.

## Slide 14: Model for Synchronous Systems
Collection of Combinational Logic blocks separated by registers
Feedback is optional
Clock signal(s) connects only to clock input of registers
Clock (CLK): steady square wave that synchronizes the system
Register: several bits of state that samples on rising edge of CLK (positive edge-triggered) or falling edge (negative edge-triggered)

## Slide 15: Maximum Clock Frequency
What is the maximum frequency of this circuit?
Max Delay = CLK-to-Q Delay + CL Delay + Setup Time
Hint:
Frequency = 1/Period

## Slide 16: Critical Paths
Timing…
Note: delay of 1 clock cycle from input to output.
Clock period limited by propagation delay of adder/shifter.

## Slide 17: Pipelining to improve performance
Timing…
Insertion of register allows higher clock frequency.
More outputs per second (higher bandwidth)
But each individual result takes longer (greater latency)

## Slide 18: Recap of Timing Terms
Clock (CLK) - steady square wave that synchronizes system
Setup Time - when the input must be stable before the rising edge of the CLK
Hold Time - when the input must be stable after the rising edge of the CLK
“CLK-to-Q” Delay - how long it takes the output to change, measured from the rising edge of the CLK
Flip-flop - one bit of state that samples every rising edge of the CLK (positive edge-triggered)
Register - several bits of state that samples on rising edge of CLK or on LOAD (positive edge-triggered)

## Slide 19: Clickers/Peer Instruction
What is maximum clock frequency? (assume all unconnected inputs come from some register)
A: 5 GHz
B: 200 MHz
C: 500 MHz
D: 1/7 GHz
E: 1/6 GHz
Clock->Q 1ns
Setup 1ns
Hold 1ns
AND delay 1ns

## Slide 20: Administrivia
Project 2-1 due 10/04
Midterm is next Tuesday 10/06, in class
  Covers up to and including lecture 8 (CALL)
  1 handwritten, double sided, 8.5”x11” cheat sheet
  We’ll give you MIPS green sheet
Review Session:
  Saturday 10/03, 11am - 1pm at 155 Dwinelle
Emails sent-out to students requiring special accommodation for the exam – please respond

## Slide 21: Study Advice
Review slides, book, worksheets, etc. and add to your cheatsheet as you do so
  This step is not the end
Take a mock exam in the allotted time, using only your cheatsheet
Go over solutions, look at why the answers are what they are (especially for questions you answered incorrectly)
Update cheatsheet as necessary
if (!perfect) goto 2;
Notes: see hkn for old exams

## Slide 22: Finite State Machines (FSM) Intro
A convenient way to conceptualize computation over time
We start at a state and given an input, we follow some edge to another (or the same) state
The function can be represented with a “state transition diagram”.
With combinational logic and registers, any FSM can be implemented in hardware.

## Slide 23: FSM Example: 3 ones…
Draw the FSM…
FSM to detect the occurrence of 3 consecutive 1’s in the input.
Assume state transitions are controlled by the clock:
on each clock cycle the machine checks the inputs and moves to a new state and produces a new output…
Input/output

## Slide 24: Hardware Implementation of FSM
+
=
?
… Therefore a register is needed to hold the a representation of which state the machine is in. Use a unique bit pattern for each state.
Combinational logic circuit is used to implement a function that maps from present state and input to next state and output.

## Slide 25: FSM Combinational Logic
1
00
1
10
0
00
0
10
0
10
1
01
0
00
0
01
0
01
1
00
0
00
0
00
Output
NS
Input
PS
Truth table…
Specify CL using a truth table

## Slide 26: Building Standard Functional Units
Data multiplexers
Arithmetic and Logic Unit
Adder/Subtractor

## Slide 27: Data Multiplexer (“Mux”) (here 2-to-1, n-bit-wide)

## Slide 28: N instances of 1-bit-wide mux
How many rows in TT?

## Slide 29: How do we build a 1-bit-wide mux?

## Slide 30: 4-to-1 multiplexer?
How many rows in TT?

## Slide 31: Another way to build 4-1 mux?
Hint: NCAA tourney!
Ans: Hierarchically!

## Slide 32: Arithmetic and Logic Unit
Most processors contain a special logic block called the “Arithmetic and Logic Unit” (ALU)
We’ll show you an easy one that does ADD, SUB, bitwise AND, bitwise OR

## Slide 33: Our simple ALU

## Slide 34: Clicker Question
Convert the truth table to a boolean expression
(no need to simplify):
A: F = xy + x(~y)
B: F = xy + (~x)y + (~x)(~y)
C: F = (~x)y + x(~y)
D: F = xy + (~x)y
E: F = (x+y)(~x+~y)
x | y | F(x,y)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 35: In the News: Microsoft, Google beat Humans at Image Recognition (EE Times)
On ImageNet benchmark image database, systems from Microsoft and Google performed better than humans at recognizing images
Both companies used deep artificial neural networks to train on image database

## Slide 36: How to design Adder/Subtractor?
Truth-table, then determine canonical form, then minimize and implement as we’ve seen before
Look at breaking the problem down into smaller pieces that we can cascade or hierarchically layer

## Slide 37: Adder/Subtractor – One-bit adder LSB…

## Slide 38: Adder/Subtractor – One-bit adder (1/2)…

## Slide 39: Adder/Subtractor – One-bit adder (2/2)

## Slide 40: N 1-bit adders  1 N-bit adder
What about overflow?
Overflow = cn?
+
+
+
b0

## Slide 41: Extremely Clever Subtractor
x | y | XOR(x,y)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
+
+
+
XOR serves as conditional inverter!

## Slide 42: In Conclusion
Finite State Machines have clocked state elements plus combinational logic to describe transition between states
  Clocks synchronize D-FF change (Setup and Hold times important!)
Standard combinational functional unit blocks built hierarchically from subcomponents