## Slide 1: CS 61C: Great Ideas in Computer Architecture Datapath
Instructors:
John Wawrzynek & Vladimir Stojanovic
http://inst.eecs.Berkeley.edu/~cs61c/fa15

## Slide 2: Components of a Computer
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
ReadData
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data

## Slide 3: The CPU
Processor (CPU): the active part of the computer that does all the work (data manipulation and decision-making)
Datapath: portion of the processor that contains hardware necessary to perform operations required by the processor (the brawn)
Control: portion of the processor (also in hardware) that tells the datapath what needs to be done (the brain)

## Slide 4: Datapath and Control
Datapath designed to support data transfers required by instructions
Controller causes correct transfers to happen
Controller
opcode, funct
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
PC

## Slide 5: Five Stages of Instruction Execution
Stage 1: Instruction Fetch
Stage 2: Instruction Decode
Stage 3: ALU (Arithmetic-Logic Unit)
Stage 4: Memory Access
Stage 5: Register Write

## Slide 6: Stages of Execution on Datapath
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write
PC
Notes: missing: multiplexors or “data selectors” – where should they be in this picture and why?
also missing – opcode for control of what operations to perform
state elements vs combinational ones – combinational given the same input will always produce the same output – out depends only on the current input

## Slide 7: Stages of Execution (1/5)
There is a wide variety of MIPS instructions: so what general steps do they have in common?
Stage 1: Instruction Fetch
  no matter what the instruction, the 32-bit instruction word must first be fetched from memory (the cache-memory hierarchy)
  also, this is where we Increment PC (that is, PC = PC + 4, to point to the next instruction: byte addressing so + 4)

## Slide 8: Stages of Execution (2/5)
Stage 2: Instruction Decode
  upon fetching the instruction, we next gather data from the fields (decode all necessary instruction data)
  first, read the opcode to determine instruction type and field lengths
  second, read in data from all necessary registers
    for add, read two registers
    for addi, read one register
    for jal, no reads necessary

## Slide 9: Stages of Execution (3/5)
Stage 3: ALU (Arithmetic-Logic Unit)
  the real work of most instructions is done here: arithmetic (+, -, *, /), shifting, logic (&, |), comparisons (slt)
  what about loads and stores?
    lw $t0, 40($t1)
    the address we are accessing in memory = the value in $t1 PLUS the value 40
    so we do this addition in this stage

## Slide 10: Stages of Execution (4/5)
Stage 4: Memory Access
  actually only the load and store instructions do anything during this stage; the others remain idle during this stage or skip it all together
  since these instructions have a unique step, we need this extra stage to account for them
  as a result of the cache system, this stage is expected to be fast

## Slide 11: Stages of Execution (5/5)
Stage 5: Register Write
  most instructions write the result of some computation into a register
  examples: arithmetic, logical, shifts, loads, slt
  what about stores, branches, jumps?
    don’t write anything into a register at the end
    these remain idle during this fifth stage or skip it all together

## Slide 12: Stages of Execution on Datapath
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write
PC
Notes: missing: multiplexors or “data selectors” – where should they be in this picture and why?
also missing – opcode for control of what operations to perform
state elements vs combinational ones – combinational given the same input will always produce the same output – out depends only on the current input

## Slide 13: Datapath Walkthroughs (1/3)
add $r3,$r1,$r2 # r3 = r1+r2
  Stage 1: fetch this instruction, increment PC
  Stage 2: decode to determine it is an add, then read registers $r1 and $r2
  Stage 3: add the two values retrieved in Stage 2
  Stage 4: idle (nothing to write to memory)
  Stage 5: write result of Stage 3 into register $r3

## Slide 14: Example: add Instruction
instruction
memory
+4
registers
ALU
Data
memory
imm
2
1
3
reg[1] + reg[2]
reg[2]
reg[1]
PC
add r3, r1, r2

## Slide 15: Datapath Walkthroughs (2/3)
slti $r3,$r1,17 # if (r1 <17 ) r3 = 1 else r3 = 0
  Stage 1: fetch this instruction, increment PC
  Stage 2: decode to determine it is an slti, then read register $r1
  Stage 3: compare value retrieved in Stage 2 with the integer 17
  Stage 4: idle
  Stage 5: write the result of Stage 3 (1 if reg source was less than signed immediate, 0 otherwise) into register $r3

## Slide 16: Example: slti Instruction
instruction
memory
+4
registers
ALU
Data
memory
imm
3
1
x
reg[1] < 17?
17
reg[1]
PC
slti r3, r1, 17

## Slide 17: Datapath Walkthroughs (3/3)
sw $r3,17($r1) # Mem[r1+17]=r3
  Stage 1: fetch this instruction, increment PC
  Stage 2: decode to determine it is a sw, then read registers $r1 and $r3
  Stage 3: add 17 to value in register $r1 (retrieved in Stage 2) to compute address
  Stage 4: write value in register $r3 (retrieved in Stage 2) into memory address computed in Stage 3
  Stage 5: idle (nothing to write into a register)

## Slide 18: Example: sw Instruction
instruction
memory
+4
registers
ALU
Data
memory
imm
3
1
x
reg[1] + 17
17
reg[1]
MEM[r1+17] = r3
reg[3]
PC
sw r3, 17(r1)

## Slide 19: Why Five Stages? (1/2)
Could we have a different number of stages?
  Yes, other ISAs have different natural number of stages
Why does MIPS have five if instructions tend to idle for at least one stage?
  Five stages are the union of all the operations needed by all the instructions.
  One instruction uses all five stages: the load

## Slide 20: Why Five Stages? (2/2)
lw $r3,17($r1) # r3=Mem[r1+17]
  Stage 1: fetch this instruction, increment PC
  Stage 2: decode to determine it is a lw, then read register $r1
  Stage 3: add 17 to value in register $r1 (retrieved in Stage 2)
  Stage 4: read value from memory address computed in Stage 3
  Stage 5: write value read in Stage 4 into register $r3

## Slide 21: Example: lw Instruction
ALU
instruction
memory
+4
registers
Data
memory
imm
3
1
x
reg[1] + 17
reg[1]
MEM[r1+17]
PC
lw r3, 17(r1)
17

## Slide 22: Clickers/Peer Instruction
Which type of MIPS instruction is active in the fewest stages?
A: LW
B: BEQ
C: J
D: JAL
E: ADDU

## Slide 23: In the News
At ISSCC 2015 in San Francisco, latest IBM mainframe chip details
z13 designed in 22nm SOI technology with seventeen metal layers, 4 billion transistors/chip
8 cores/chip, with 2MB L2 cache, 64MB L3 cache, and 480MB L4 cache.
5GHz clock rate, 6 instructions per cycle, 2 threads/core
Up to 24 processor chips in shared memory node

## Slide 24: Processor Design: 5 steps
  Step 1: Analyze instruction set to determine datapath requirements
  Meaning of each instruction is given by register transfers
  Datapath must include storage element for ISA registers
  Datapath must support each register transfer
  Step 2: Select set of datapath components & establish clock methodology
  Step 3: Assemble datapath components that meet the requirements
  Step 4: Analyze implementation of each instruction to determine setting of control points that realizes the register transfer
  Step 5: Assemble the control logic

## Slide 25: The MIPS Instruction Formats
All MIPS instructions are 32 bits long. 3 formats:
  R-type
  I-type
  J-type
The different fields are:
  op: operation (“opcode”) of the instruction
  rs, rt, rd: the source and destination register specifiers
  shamt: shift amount
  funct: selects the variant of the operation in the “op” field
  address / immediate: address offset or immediate value
  target address: target address of jump instruction
op
target address
0
26
31
6 bits
26 bits
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
address/immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Notes: One of the most important thing you need to know before you start designing a processor is how the instructions look like.
Or in more technical term, you need to know the instruction format. One good thing about the MIPS instruction set is that it is very simple.
First of all, all MIPS instructions are 32 bits long and there are only three instruction formats: (a) R-type, (b) I-type, and (c) J-type.
The different fields of the R-type instructions are:
(a) OP specifies the operation of the instruction.
(b) Rs, Rt, and Rd are the source and destination register specifiers.
(c) Shamt specifies the amount you need to shift for the shift instructions.
(d) Funct selects the variant of the operation specified in the “op” field.
For the I-type instruction, bits 0 to 15 are used as an immediate field. I will show you how this immediate field is used differently by different instructions.
Finally for the J-type instruction, bits 0 to 25 become the target address of the jump.
+3 = 10 min. (X:50)

## Slide 26: The MIPS-lite Subset
ADDU and SUBU
  addu rd,rs,rt
  subu rd,rs,rt
OR Immediate:
  ori rt,rs,imm16
LOAD and STORE Word
  lw rt,rs,imm16
  sw rt,rs,imm16
BRANCH:
  beq rs,rt,imm16
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Notes: In today’s lecture, I will show you how to implement the following subset of MIPS instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register. (Note that dest is the Rt field!)
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to from the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specified the registers we need to compare.
If these two registers are equal, we will branch to a location offset by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.
start at 7min

## Slide 27: Register Transfer Level (RTL)
Colloquially called “Register Transfer Language”
RTL gives the meaning of the instructions
All start by fetching the instruction itself
{op , rs , rt , rd , shamt , funct}  MEM[ PC ]
{op , rs , rt , Imm16}  MEM[ PC ]
Inst Register Transfers
ADDU R[rd]  R[rs] + R[rt]; PC  PC + 4
SUBU R[rd]  R[rs] – R[rt]; PC  PC + 4
ORI R[rt]  R[rs] | zero_ext(Imm16); PC  PC + 4
LOAD R[rt]  MEM[ R[rs] + sign_ext(Imm16)]; PC  PC + 4
STORE MEM[ R[rs] + sign_ext(Imm16) ]  R[rt]; PC  PC + 4
BEQ if ( R[rs] == R[rt] ) PC  PC + 4 + {sign_ext(Imm16), 2’b00}
else PC  PC + 4
Notes: RTL – like most programming langs:
precise and unambiguous
must be debugged
code can be checked automatically for certain properties – type checking, check against abstract state machine, etc.
TOOLS – simulator, processor, tape out
Verilog is a popular RTL (used in 150 for FPGA development)
10 mins

## Slide 28: Step 1: Requirements of the Instruction Set
Memory (MEM)
  Instructions & data (will use one for each)
Registers (R: 32, 32-bit wide registers)
  Read RS
  Read RT
  Write RT or RD
Program Counter (PC)
Extender (sign/zero extend)
Add/Sub/OR/etc unit for operation on register(s) or extended immediate (ALU)
Add 4 (+ maybe extended immediate) to PC
Compare registers?
Notes: 15 mins

## Slide 29: Step 2: Components of the Datapath
Combinational Elements
Storage Elements + Clocking Methodology
Building Blocks
32
32
A
B
32
Sum
CarryOut
CarryIn
Adder
32
A
B
32
Y
32
Select
MUX
Multiplexer
32
32
A
B
32
Result
OP
ALU
ALU
Adder
Notes: Adder – why no overflow detect?
Multiplexer – talk about specs – width of data multiplexed, # of select bits

## Slide 30: ALU Needs for MIPS-lite + Rest of MIPS
Addition, subtraction, logical OR, ==:
  ADDU R[rd] = R[rs] + R[rt]; ...
  SUBU R[rd] = R[rs] – R[rt]; ...
  ORI R[rt] = R[rs] | zero_ext(Imm16)...
  BEQ if ( R[rs] == R[rt] )...
Test to see if output == 0 for any ALU operation gives == test. How?
P&H also adds AND, Set Less Than (1 if A < B, 0 otherwise)
ALU follows Chapter 5
Notes: 20 mins

## Slide 31: Storage Element: Idealized Memory
“Magic” Memory
  One input bus: Data In
  One output bus: Data Out
Memory word is found by:
  For Read: Address selects the word to put on Data Out
  For Write: Set Write Enable = 1: address selects the memory word to be written via the Data In bus
Clock input (CLK)
  CLK input is a factor ONLY during write operation
  During read operation, behaves as a combinational logic block: Address valid  Data Out valid after “access time”
Clk
Data In
Write Enable
32
32
DataOut
Address
Notes: The last storage element you will need for the datapath is the idealized memory to store your data and instructions.
This idealized memory block has just one input bus (DataIn) and one output bus (DataOut).
When Write Enable is 0, the address selects the memory word to put on the Data Out bus.
When Write Enable is 1, the address selects the memory word to be written via the DataIn bus at the next clock tick.
Once again, the clock input is a factor ONLY during the write operation.
During read operation, it behaves as a combinational logic block.
That is if you put a valid value on the address lines, the output bus DataOut will become valid after the access time of the memory.
+2 = 35 min. (Y:15)

## Slide 32: Storage Element: Register (Building Block)
Similar to D Flip Flop except
  N-bit input and output
  Write Enable input
Write Enable:
  Negated (or deasserted) (0): Data Out will not change
  Asserted (1): Data Out will become Data In on positive edge of clock
clk
Data In
Write Enable
N
N
Data Out
Notes: As far as storage elements are concerned, we will need a N-bit register that is similar to the D flip-flop I showed you in class.
The significant difference here is that the register will have a Write Enable input.
That is the content of the register will NOT be updated if Write Enable is not asserted (0).
The content is updated at the clock tick ONLY if the Write Enable signal is asserted (1).
Show how to build Register from FF
25 mins

## Slide 33: Storage Element: Register File
Register File consists of 32 registers:
  Two 32-bit output busses:
  busA and busB
  One 32-bit input bus: busW
Register is selected by:
  RA (number) selects the register to put on busA (data)
  RB (number) selects the register to put on busB (data)
  RW (number) selects the register to be written via busW (data) when Write Enable is 1
Clock input (clk)
  Clk input is a factor ONLY during write operation
  During read operation, behaves as a combinational logic block:
    RA or RB valid  busA or busB valid after “access time.”
Clk
busW
Write Enable
32
32
busA
32
busB
5
5
5
RW
RA
RB
32 x 32-bit
Registers
Notes: We will also need a register file that consists of 32 32-bit registers with two output busses (busA and busB) and one input bus.
The register specifiers Ra and Rb select the registers to put on busA and busB respectively.
When Write Enable is 1, the register specifier Rw selects the register to be written via busW.
In our simplified version of the register file, the write operation will occurs at the clock tick.
Keep in mind that the clock input is a factor ONLY during the write operation.
During read operation, the register file behaves as a combinational logic block.
That is if you put a valid value on Ra, then bus A will become valid after the register file’s access time.
Similarly if you put a valid value on Rb, bus B will become valid after the register file’s access time. In both cases (Ra and Rb), the clock input is not a factor.
+2 = 33 min. (Y:13)

## Slide 34: Step 3a: Instruction Fetch Unit
Register Transfer Requirements  Datapath Assembly
Instruction Fetch
Read Operands and Execute Operation
Common RTL operations
  Fetch the Instruction: mem[PC]
  Update the program counter:
    Sequential Code: PC  PC + 4
    Branch and Jump: PC  “something else”
32
Instruction Word
Address
Instruction
Memory
PC
clk
Next Address
Logic

## Slide 35: Step 3b: Add & Subtract
R[rd] = R[rs] op R[rt] (addu rd,rs,rt)
  Ra, Rb, and Rw come from instruction’s Rs, Rt, and Rd fields
  ALUctr and RegWr: control logic after decoding the instruction
… Already defined the register file & ALU
32
Result
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 x 32-bit
Registers
Rs
Rt
Rd
ALU
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
Notes: And here is the datapath that can do the trick.
First of all, we connect the register file’s Ra, Rb, and Rw input to the Rd, Rs, and Rt fields of the instruction bus (points to the format diagram).
Then we need to connect busA and busB of the register file to the ALU.
Finally, we need to connect the output of the ALU to the input bus of the register file.
Conceptually, this is how it works.
The instruction bus coming out of the Instruction memory will set the Ra and Rb to the register specifiers Rs and Rt.
This causes the register file to put the value of register Rs onto busA and the value of register Rt onto busB, respectively.
By setting the ALUctr appropriately, the ALU will perform either the Add and Subtract for us.
The result is then fed back to the register file where the register specifier Rw should already be set to the instruction bus’s Rd field.
Since the control, which we will design in our next lecture, should have already set the RegWr signal to 1, the result will be written back to the register file at the next clock tick (points to the Clk input).
30 mins

## Slide 36: Clocking Methodology
Storage elements clocked by same edge
Flip-flops (FFs) and combinational logic have some delays
  Gates: delay from input change to output change
  Signals at FF D input must be stable before active clock edge to allow signal to travel within the FF (set-up time), and we have the usual clock-to-Q delay
“Critical path” (longest path through logic) determines length of clock period
Clk
.
.
.
.
.
.
.
.
.
.
.
.
Notes: Remember, we will be using a clocking methodology where all storage elements are clocked by the same clock edge.
Consequently, our cycle time will be the sum of:
(a) The Clock-to-Q time of the input registers.
(b) The longest delay path through the combinational logic block.
(c) The set up time of the output register.
(d) And finally the clock skew.
In order to avoid hold time violation, you have to make sure this inequality is fulfilled.
+2 = 18 min. (X:58)

## Slide 37: Register-Register Timing: One Complete Cycle
Clk
PC
Rs, Rt, Rd,
Op, Func
ALUctr
Instruction Memory Access Time
Old Value
New Value
RegWr
Old Value
New Value
Delay through Control Logic
busA, B
Register File Access Time
Old Value
New Value
busW
ALU Delay
Old Value
New Value
Old Value
New Value
New Value
Old Value
Register Write
Occurs Here
32
ALUctr
clk
busW
RegWr
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
ALU
5
Rd
Notes: Let’s take a more quantitative picture of what is happening.
At each clock tick, the Program Counter will present its latest value to the Instruction memory after Clk-to-Q time.
After a delay of the Instruction Memory Access time, the Opcode, Rd, Rs, Rt, and Function fields will become valid on the instruction bus.
Once we have the new instruction, that is the Add or Subtract instruction, on the instruction bus, two things happen in parallel.
First of all, the control unit will decode the Opcode and Func field and set the control signals ALUctr and RegWr accordingly. We will cover this in the next lecture.
While this is happening (points to Control Delay), we will also be reading the register file (Register File Access Time).
Once the data is valid on busA and busB, the ALU will perform the Add or Subtract operation based on the ALUctr signal.
Hopefully, the ALU is fast enough that it will finish the operation (ALU Delay) before the next clock tick.
At the next clock tick, the output of the ALU will be written into the register file because the RegWr signal will be equal to 1.
+3 = 45 min. (Y:25)

## Slide 38: Putting it All Together:A Single Cycle Datapath
imm16
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
Equal
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
clk
PC
00
4
nPC_sel
PC Ext
Adr
Inst
Memory
Adder
Adder
Mux
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5
Notes: So here is the single cycle datapath we just built.
If you push into the Instruction Fetch Unit, you will see the last slide showing the PC, the next address logic, and the Instruction Memory.
Here I have shown how we can get the Rt, Rs, Rd, and Imm16 fields out of the 32-bit instruction word.
The Rt, Rs, and Rd fields will go to the register file as register specifiers while the Imm16 field will go to the Extender where it is either Zero and Sign extended to 32 bits.
The signals ExtOp, ALUSrc, ALUctr, MemWr, MemtoReg, RegDst, RegWr, Branch, and Jump are control signals.
And I will show you how to generate them on Friday.
+2 = 80 min. (Z:00)

## Slide 39: In Conclusion
“Divide and Conquer” to build complex logic blocks from smaller simpler pieces (adder)
Five stages of MIPS instruction execution
Mapping instructions to datapath components
Single long clock cycle per instruction