## Slide 1: CS 61C: Great Ideas in Computer Architecture Virtual Memory
Instructors:
John Wawrzynek & Vladimir Stojanovic
http://inst.eecs.berkeley.edu/~cs61c/

## Slide 2: Review
Programmed I/O
Polling vs. Interrupts
Booting a Computer
  BIOS, Bootloader, OS Boot, Init
Supervisor Mode, Syscalls
Base and Bounds
  Simple, but doesn’t give us everything we want
Intro to VM

## Slide 3: Traps/Interrupts/Execeptions: altering the normal flow of control
Ii-1
HI1
HI2
HIn
Ii
Ii+1
program
trap
handler
An external or internal event that needs to be processed - by another program – the OS. The event is often unexpected from original program’s point of view.

## Slide 4: Terminology
In CS61C (you’ll see other definitions in use elsewhere):
Interrupt – caused by an event external to current running program (e.g. key press, mouse activity)
  Asynchronous to current program, can handle interrupt on any convenient instruction
Exception – caused by some event during execution of one instruction of current running program (e.g., bus error, illegal instruction)
  Synchronous, must handle exception on instruction that causes exception
Trap – action of servicing interrupt or exception by hardware jump to “trap handler” code

## Slide 5: Precise Traps
Trap handler’s view of machine state is that every instruction prior to the trapped one has completed, and no instruction after the trap has executed.
Implies that handler can return from an interrupt by restoring user registers and jumping back to interrupted instruction (EPC register will hold the instruction address)
  Interrupt handler software doesn’t need to understand the pipeline of the machine, or what program was doing!
  More complex to handle trap caused by an exception than interrupt
Providing precise traps is tricky in a pipelined superscalar out-of-order processor!
  But handling imprecise interrupts in software is even worse.

## Slide 6: Trap Handling in 5-Stage Pipeline
How to handle multiple simultaneous exceptions in different pipeline stages?
How and where to handle external asynchronous interrupts?
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous Interrupts

## Slide 7: Save Exceptions Until Commit
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous
Interrupts
Exc
D
PC
D
Exc
E
PC
E
Exc
M
PC
M
Cause
EPC
Kill D Stage
Kill F Stage
Kill E Stage
Select Handler PC
Kill Writeback
Commit Point

## Slide 8: Handling Traps in In-Order Pipeline
Hold exception flags in pipeline until commit point (M stage)
Exceptions in earlier instructions override exceptions in later instructions
Exceptions in earlier pipe stages override later exceptions for a given instruction
Inject external interrupts at commit point (override others)
If exception/interrupt at commit: update Cause and EPC registers, kill all stages, inject handler PC into fetch stage

## Slide 9: Trap Pipeline Diagram
      time
      t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) 096: ADD IF1 ID1 EX1 MA1 - overflow!
(I2) 100: XOR IF2 ID2 EX2 - -
(I3) 104: SUB IF3 ID3 - - -
(I4) 108: ADD IF4 - - - -
(I5) Trap Handler code IF5 ID5 EX5 MA5 WB5

## Slide 10: In the News …

## Slide 11: Virtual Memory

## Slide 12: “Bare” 5-Stage Pipeline
In a bare machine, the only kind of address is a physical address
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Physical Address

## Slide 13: What do we need Virtual Memory for? Reason 1: Adding Disks to Hierarchy
Need to devise a mechanism to “connect” memory and disk in the memory hierarchy

## Slide 14: What do we need Virtual Memory for? Reason 2: Simplifying Memory for Apps
Applications should see the straightforward memory layout we saw earlier ->
User-space applications should think they own all of memory
So we give them a virtual view of memory
code
static data
heap
stack
~ 7FFF FFFFhex
~ 0000 0000hex
Notes: Location independent automatically

## Slide 15: What do we need Virtual Memory for? Reason 3: Protection Between Processes
With a bare system, addresses issued with loads/stores are real physical addresses
This means any program can issue any address, therefore can access any part of memory, even areas which it doesn’t own
  Ex: The OS data structures
We should send all addresses through a mechanism that the OS controls, before they make it out to DRAM - a translation mechanism

## Slide 16: Address Spaces
The set of addresses labeling all of memory that we can access
Now, 2 kinds:
  Virtual Address Space - the set of addresses that the user program knows about
  Physical Address Space - the set of addresses that map to actual physical cells in memory
    Hidden from user applications
So, we need a way to map between these two address spaces
Notes: because the programs will issue virtual addresses, but we need physical addresses to access data in DRAM

## Slide 17: Blocks vs. Pages
In caches, we dealt with individual blocks
  Usually ~64B on modern systems
  We could “divide” memory into a set of blocks
In VM, we deal with individual pages
  Usually ~4 KB on modern systems
  Now, we’ll “divide” memory into a set of pages
Common point of confusion: Bytes, Words, Blocks, Pages are all just different ways of looking at memory!

## Slide 18: Bytes, Words, Blocks, Pages
Ex: 16 KiB DRAM, 4 KiB Pages (for VM), 128 B blocks (for caches), 4 B words (for lw/sw)
Page 3
Page 2
Page 1
Page 0
16 KiB
Block 0
Block 31
Word 0
Word 31
1 Memory
1 Page
1 Block
Can think of memory as:
- 4 Pages
OR
- 128 Blocks
OR
- 4096 Words
Can think of a page as:
- 32 Blocks
OR
- 1024 Words

## Slide 19: Address Translation
So, what do we want to achieve at the hardware level?
  Take a Virtual Address, that points to a spot in the Virtual Address Space of a particular program, and map it to a Physical Address, which points to a physical spot in DRAM of the whole machine
Virtual Page Number | Offset
Virtual Address
Physical Address
Physical Page Number | Offset

## Slide 20: Address Translation
Virtual Page Number | Offset
Physical Page Number | Offset
Virtual Address
Physical Address
Address Translation
Copy Bits
The rest of the lecture is all about implementing
Notes: Phys addr will then go to the cache just like before, cache will split that same addr into TIO. you can think of them completely separately for now. caches work just like before

## Slide 21: Paged Memory Systems
Processor-generated address can be split into:
Page tables make it possible to store the pages of a program non-contiguously.
0
1
2
3
0
1
2
3
Address Space
of Program #1
Page Table
of Program #1
1
0
2
3
Physical Memory
A page table contains the physical address of the base of each page
Virtual Page Number | Offset
Notes: Relaxes the contiguous allocation requirement.

## Slide 22: Private (Virtual) Address Space per Program
VA1
Prog 1
Page Table
VA1
Prog 2
Page Table
VA1
Prog 3
Page Table
Physical Memory
free
OS
pages
Each prog has a page table
Page table contains an entry for each prog page
Physical Memory acts like a “cache” of pages for currently running programs. Not recently used pages are stored in secondary memory, e.g. disk (in “swap partition”)
Notes: Pages are fixed sized chunks. So no fragmentation in terms of pages

## Slide 23: Where Should Page Tables Reside?
Space required by the page tables (PT) is proportional to the address space, number of users, ...
    Too large to keep in registers inside CPU
Idea: Keep page tables in the main memory
  Needs one reference to retrieve the page base address and another to access the data word
   doubles the number of memory references! (but we can fix this using something we already know about…)
Notes: for each program, keep track of the PHYSICAL ADDRESS of the start of the page table inside the CPU

## Slide 24: Page Tables in Physical Memory
VA1
Prog 1 Virtual Address Space
Prog 2 Virtual Address Space
PT Prog1
PT Prog2
VA1
Physical Memory

## Slide 25: MT2 Grades Posted
62%

## Slide 26: Administrivia
Upcoming Lecture Schedule
  11/19: VM (today)
  11/24: I/O: DMA, Disks, Networking
  11/26: Thanksgiving Holiday (no class)
  12/01: Dependability: Parity, ECC, RAID
    Last day of new material
  12/03: Summary, What’s Next? (+ HKN reviews)

## Slide 27: Administrivia
Okay to turn-in HW4 today (without slip charge)
Project 4 programming competition rules posted.
  Competition will end 11/30.
Last HW (5) Virtual Memory
  Due 12/06 (Sunday after end of classes)
Last project (5): Spark
  5-1: posted, due 11/24 (next Wednesday)
  5-2: due 12/06 (Sunday after end of classes)
Final Exam is Friday (12/18)
  7-10PM, RSF Field House
  More info soon on review sessions, etc.

## Slide 28: Linear (simple) Page Table
VPN
Offset
Virtual address
PT Base Register
VPN
Data word
Data Pages
Offset
PPN
PPN
DPN
PPN
PPN
PPN
Page Table
DPN
PPN
DPN
DPN
DPN
PPN
Page Table Entry (PTE) contains:
  1 bit to indicate if page exists
  And either PPN or DPN:
  PPN (physical page number) for a memory-resident page
  DPN (disk page number) for a page on the disk
  Status bits for protection and usage (read, write, exec)
OS sets the Page Table Base Register whenever active user process changes

## Slide 29: Suppose an instruction references a memory page that isn’t in DRAM?
We get a exception of type “page fault”
Page fault handler does the following:
  If virtual page doesn’t yet exist, assign an unused page in DRAM, or if page exists …
  Initiate transfer of the page we’re requesting from disk to DRAM, assigning to an unused page
  If no unused page is left, a page currently in DRAM is selected to be replaced (based on usage)
  The replaced page is written (back) to disk, page table entry that maps that VPN->PPN is marked as invalid/DPN
  Page table entry of the page we’re requesting is updated with a (now) valid PPN

## Slide 30: Size of Linear Page Table
With 32-bit memory addresses, 4-KB pages:
  232 / 212 = 220 virtual pages per user, assuming 4-Byte PTEs,
  220 PTEs, i.e, 4 MB page table per user!
Larger pages?
  Internal fragmentation (Not all memory in page gets used)
  Larger page fault penalty (more time to read from disk)
What about 64-bit virtual address space???
  Even 1MB pages would require 244 8-Byte PTEs (35 TB!)
What is the “saving grace” ? Most processes only use a set of high address (stack), and a set of low address (instructions, heap)
Notes: Virtual address space is large but only a small fraction of the
pages are populated. So we can use a sparse representation
of the table.

## Slide 31: Hierarchical Page Table – exploits sparcity of virtual address space use
Level 1
Page Table
Level 2
Page Tables
Data Pages
page in primary memory
page in secondary memory
Root of the Current
Page Table
p1
p2
Virtual Address
(Processor
Register)
PTE of a nonexistent page
p1 p2 offset
0
11
12
21
22
31
10-bit
L1 index
10-bit
L2 index
Physical Memory

## Slide 32: Address Translation & Protection
Every instruction and data access needs address
translation and protection checks
A good VM design needs to be fast (~ one cycle) and space efficient
Physical Address
Virtual Address
Address
Translation
Virtual Page No. (VPN)
offset
Physical Page No. (PPN)
offset
Protection
Check
Exception?
Kernel/User Mode
Read/Write

## Slide 33: Translation Lookaside Buffers (TLB)
Address translation is very expensive!
  In a two-level page table, each reference becomes several memory accesses
Solution: Cache some translations in TLB
TLB hit  Single-Cycle Translation
TLB miss  Page-Table Walk to refill
VPN offset
V R W D tag PPN
physical address
PPN offset
virtual address
hit?
(VPN = virtual page number)
(PPN = physical page number)
Notes: 3 memory references
2 page faults (disk accesses) + ..
Actually used in IBM before paged memory.

## Slide 34: TLB Designs
Typically 32-128 entries, usually fully associative
  Each entry maps a large page, hence less spatial locality across pages => more likely that two entries conflict
  Sometimes larger TLBs (256-512 entries) are 4-8 way set-associative
  Larger systems sometimes have multi-level (L1 and L2) TLBs
Random or FIFO replacement policy
“TLB Reach”: Size of largest virtual address space that can be simultaneously mapped by TLB
  Example: 64 TLB entries, 4KB pages, one page per entry
  TLB Reach = _____________________________________________?
Notes: 256 KiB mapped at once in the TLB

## Slide 35: VM-related events in pipeline
Handling a TLB miss needs a hardware or software mechanism to refill TLB
  usually done in hardware now
Handling a page fault (e.g., page is on disk) needs a precise trap so software handler can easily resume after retrieving page
Handling protection violation may abort process
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+
TLB miss? Page Fault?
Protection violation?
TLB miss? Page Fault?
Protection violation?

## Slide 36: Hierarchical Page Table Walk: SPARC v8
31 11 0
Virtual Address
Index 1 Index 2 Index 3 Offset
31 23 17 11 0
Context
Table
Register
Context
Register
root ptr
PTP
PTP
PTE
Context Table
L1 Table
L2 Table
L3 Table
Physical Address
PPN Offset
MMU does this table walk in hardware on a TLB miss

## Slide 37: Page-Based Virtual-Memory Machine (Hardware Page-Table Walk)
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Page Fault?
Protection violation?
Page Fault?
Protection violation?
Assumes page tables held in untranslated physical memory
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Physical Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?

## Slide 38: Address Translation: putting it all together
Virtual Address
TLB
Lookup
Page Table
Walk
Update TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
(to cache)
miss
hit
the page is
Ï memory Î memory
denied
permitted
Protection
Fault
hardware
hardware or software
software
SEGFAULT
Where?
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 39: Modern Virtual Memory Systems Illusion of a large, private, uniform store
Protection & Privacy
  several users, each with their private address space and one or more shared address spaces
page table  name space
Demand Paging
  Provides the ability to run programs larger than the primary memory
  Hides differences in machine configurations
The price is address translation on
each memory reference
OS
useri
Primary
Memory
Swapping Store
(Disk)
VA
PA
mapping
TLB
Notes: Portability on machines with different memory configurations.

## Slide 40: Clicker Question
Let’s try to extrapolate from caches… Which one is false?
A. # offset bits in V.A. = log2(page size)
B. # offset bits in P.A. = log2(page size)
C. # VPN bits in V.A. = log2(# of physical pages)
D. # PPN bits in P.A. = log2(# of physical pages)
E. A single-level page table contains a PTE for every possible VPN in the system
Notes: C. it’s the # of virtual pages, which is != to # of physical pages

## Slide 41: Conclusion: VM features track historical uses
Bare machine, only physical addresses
  One program owned entire machine
Batch-style multiprogramming
  Several programs sharing CPU while waiting for I/O
  Base & bound: translation and protection between programs (not virtual memory)
  Problem with external fragmentation (holes in memory), needed occasional memory defragmentation as new jobs arrived
Time sharing
  More interactive programs, waiting for user. Also, more jobs/second.
  Motivated move to fixed-size page translation and protection, no external fragmentation (but now internal fragmentation, wasted bytes in page)
  Motivated adoption of virtual memory to allow more jobs to share limited physical memory resources while holding working set in memory
Virtual Machine Monitors
  Run multiple operating systems on one machine
  Idea from 1970s IBM mainframes, now common on laptops
    e.g., run Windows on top of Mac OS X
  Hardware support for two levels of translation/protection
    Guest OS virtual -> Guest OS physical -> Host machine physical
  Also basis of Cloud Computing
    Virtual machine instances on EC2 for Lab 13